LabFriend Manual

# Connectors
Hhh
'
Pin Number	Function
1	CMPMEAS, Component measurement pin (caps inductors, resistors)
2	EXVO, Voltage output, max 50mA 5V (adjustable)
3	GND
4	GND
5	AOUTR, High Resolution AF channel 1 output
6	AOUTL, High Resolution AF channel 2 output
7	AINR, High Resolution AF channel 1 input
8	AINL, High Resolution AF channel 2 input
9	GND
10	GND
11	HFDAC, 3MHz DAC out, 8 bit 0 - 5V
12	GND
13	GND
14	DCMEAS3, DC measurement 0-5V 16bit +gain
15	DCMEAS1, DC measurement 0-5V 16bit +gain (can be used with channel 2 in diff m)
15	DCMEAS2, DC measurement 0-5V 16bit +gain